## Slide 1
Fourier Neural Operator for Parametric Darcy Flow
AE646: Scientific Machine Learning for Fluid Mechanics Project Theme #8 - Operator Learning for Parametric PDEs
Team PINNacles
Aryamann Srivastava • Varun Sathaye • Atishay Jain • Vedant S. Tiwari
IIT Kanpur | Semester 2026–27-I | Dr. Sathesh Mariappan

## Slide 2
Problem Statement
2D Darcy flow - steady-state pressure in a heterogeneous porous medium
AE646 | PINNacles | Stage 1 Proposal
2 / 10
The Governing Equation
−∇·( κ(x,y) ∇u(x,y) ) = f(x,y) on (0,1)²
u = 0 on boundary, f = β = 1.0
κ(x,y) = permeability field | u(x,y) = pressure solution
The Challenge
• Traditional solvers (FDM/FEM) re-solve for every new κ field
• Each solve: ~1 second for a simple 2D case
• Optimization or UQ needs thousands of solves → impractical
Objective
Learn the solution operator G : κ(x,y) → u(x,y) once. Evaluate any new permeability field in milliseconds - no re-solving needed. Enables fast parametric studies, optimization, and uncertainty quantification.

## Slide 3
Dataset
PDEBench 2D Darcy Flow (β=1.0) - official, checksum-verified source
AE646 | PINNacles | Stage 1 Proposal
3 / 10
Official Source
DaRUS / University of Stuttgart DOI: 10.18419/darus-2986 10,000 samples at native 128×128 resolution
Our Reproducible Subset (seed = 42)
Train: 900 samples Validation: 100 samples Test: 200 samples (held out) Main resolution: 64×64 (stride-2 downsample)
Permeability κ(x,y)
Piecewise-constant: values in {0.1, 1.0} Generated by thresholding a smooth Gaussian random field at zero Produces sharp-boundary blob patterns in 2D
Why 64×64?
Standard resolution for FNO Darcy experiments Retains full PDE spatial structure FNO can then be tested at 128×128 zero-shot - no retraining needed
Super-Res Hold-out
200 test samples also kept at native 128×128 Used only for zero-shot evaluation Never seen by the model during training in any form

## Slide 4
Baseline Method: MLP
Dense fully-connected network - no spatial inductive bias
AE646 | PINNacles | Stage 1 Proposal
4 / 10
Input 64×64×3
→
Flatten →12,288
→
Linear 2048 +GELU
→
Linear 2048 +GELU
→
Linear 2048 +GELU
→
Linear 4096 +Reshape
→
Output 64×64×1
Architecture Details
• 42.0M trainable parameters
• Input: [permeability, x_coord, y_coord] - 3 channels
• 3 hidden layers × 2048 units, GELU activation
• Output: flat 64×64, reshaped to grid
Why This as Baseline?
• Treats all 4096 output pixels independently
• No spatial locality or translation equivariance
• Fixed 64×64 I/O - cannot evaluate at any other resolution
• Establishes a clear performance floor for comparison
Key limitation: the MLP has hard-coded 64×64 input/output dimensions - it cannot be evaluated zero-shot at any other resolution. This is in direct contrast to the FNO.

## Slide 5
Proposed SciML Method: Fourier Neural Operator
Operator learning via spectral convolutions - resolution-invariant by construction
AE646 | PINNacles | Stage 1 Proposal
5 / 10
Input 64×64×3
→
Lift 3→64
→
SpectralConv Block ×4
→
FFT→W→IFFT +Conv1×1 +LN+GELU
→
Project 64→128→1
→
Output 64×64×1
How Spectral Convolution Works
1. Apply 2D FFT → frequency domain representation
2. Keep only the lowest 12×12 Fourier modes
3. Multiply by learned complex weights (learning in Fourier space)
4. Inverse FFT → back to physical space
5. Add 1×1 Conv bypass, normalize, activate (GELU)
Key Properties
• 4.7M parameters - 8.8× fewer than MLP
• Resolution-invariant: weights don't depend on grid size
  ◦ → Evaluates at 128×128 zero-shot, no retraining
• Spectral inductive bias: Darcy pressure is low-frequency dominated
• Also training a larger config:
  ◦ → width=128, modes=20, 6 layers - 78.8M params
  ◦ → Studies accuracy vs parameter-count trade-off

## Slide 6
Evaluation Plan
Metrics, expected results, and planned figures
AE646 | PINNacles | Stage 1 Proposal
6 / 10
Primary Metric - Relative L2 Error (physical units)
‖ prediction − truth ‖₂ / ‖ truth ‖₂ computed after denormalizing to physical pressure units
Relative L2 Error
Mean / median / std / min / max across all 200 test samples
Zero-Shot Super-Res
FNO at native 128×128 vs real PDEBench ground truth - no retraining
Inference Speed
Wall-clock time vs FDM numerical solver - measured, not asserted
Qualitative Plots
κ input | target u | prediction | absolute error maps
Literature Reference & Expected Range
Li et al. 2021 (original FNO paper) reports ~0.01–0.02 relative L2 on Darcy flow. Their dataset uses smooth, continuous log-permeability (κ = exp(GRF)). PDEBench uses piecewise-constant κ ∈ {0.1, 1.0} - sharper interfaces, a harder variant. Some deviation from the literature number is expected and will be discussed.

## Slide 7
Expected Figures & Tables
Planned deliverables for Stage 2 and Stage 3 reports
AE646 | PINNacles | Stage 1 Proposal
7 / 10
1. Error Histograms
Per-sample relative L2 for FNO original, FNO improved, and MLP baseline. Reveals mean, median, and tail behaviour.
[ Figure ]
2. Sample Predictions
Side-by-side: κ input, target u, FNO prediction, absolute error. Shown for several representative test cases.
[ Figure ]
3. Model Comparison Table
Rel L2 (mean/median), parameter count, and inference time for all three models in one table.
[ Figure ]
4. Zero-Shot Super-Res
FNO evaluated at native 128x128 vs PDEBench ground truth. No retraining - validates resolution-invariance.
[ Figure ]
5. Efficiency Scatter
Rel L2 vs parameter count - one point per model. Shows the accuracy vs model-size trade-off.
[ Figure ]

## Slide 8
Work Plan
Three-stage project timeline - Stage 1 complete
AE646 | PINNacles | Stage 1 Proposal
8 / 10
Stage 1
✓ DONE
Project Proposal
Due: Aug 27, 2026
✓ Confirm PDEBench as dataset (source verified)
✓ Finalize MLP and FNO architecture design
✓ Define evaluation methodology and metrics
✓ Submit proposal PDF and presentation
Stage 2
UPCOMING
Implementation & Interim Results
Due: Sep 8, 2026
→ Set up data download and preprocessing pipeline
→ Implement and train MLP baseline
→ Implement and train FNO (original config)
→ Gather preliminary results and plots
Stage 3
PLANNED
Final Report, Code & Viva
Due: Nov 13, 2026
→ Train improved FNO (width=128, modes=20)
→ Zero-shot super-resolution at 128×128
→ Inference speed benchmark vs FDM solver
→ Final report, code submission, viva

## Slide 9
Individual Contributions
Team PINNacles - Group of 4
AE646 | PINNacles | Stage 1 Proposal
9 / 10
Aryamann Srivastava
• Model implementation (FNO and MLP)
• Training and evaluation pipelines
• Data download and preprocessing
• Benchmarks and report drafting
Varun Sathaye
• Literature review
• Baseline model tuning
• Error analysis
• Formatting deliverables
Atishay Jain
• Data visualization and plotting
• Error distribution figures
• Field comparison plots
• Slide preparation
Vedant S. Tiwari
• Zero-shot super-res testing
• Speed benchmarking
• Cross-checking results
• Proofreading final report
AI Tool Use Declaration
Claude / ChatGPT used for conceptual understanding, coding assistance, debugging, and report drafting. All output inspected, verified, and fully understood by the team before submission - in accordance with AE646's academic integrity policy.

## Slide 10
Summary
Problem
2D Darcy flow - learn G: κ → u to replace repeated PDE solves
Dataset
Real PDEBench 2D Darcy (β=1.0) | 900 / 100 / 200 split at 64×64
Baseline
MLP (42M params) - no spatial inductive bias, fixed resolution
SciML
FNO (4.7M params) - spectral convolutions, resolution-invariant
Extended
Larger FNO (78.8M params) - accuracy vs parameter-count trade-off
Evaluation
Rel L2 error | zero-shot super-res at 128×128 | speed vs FDM
Thank you - Questions welcome